## Slide 1: TSRI 教育性晶片下線流程
2020 年 9月 23日
Student Sih-Yun Chen
Professor Ming-Bo Lin

## Slide 2: Flow Chart
Implementation
Logic Synthesis
(DC)
Automatic
Place & Route
(ICC)
RTL code
Gate-level netlist
Post layout
Gate-level netlist
GDS layout
.v
_syn.v
_pr.v
.gds
(下線晶片用檔)
Tape out
(包bounding pad)
RTL Simulation
Lint Check
Code Coverage Analysis
Gate-level Simulation
(pre-sim)
Static Timing Analysis
Power Analysis
Gate-level Simulation
(post-sim)
Static Timing Analysis
Power Analysis
Transistor-level Simulation
Transistor-level STA
Power Analysis
Formal
Formal
LVS
DRC
Extraction
Transistor netlist
Verification

## Slide 3: ICC後步驟
Implementation
Add Bounding Pad
LVS
Qentry DRC
TSRI下線申請
Test Pattern
_merge.gds
lvs.rep
drc.rep
資料上傳
V93000機台測試
檢查correct
至http://www2.cic.org.tw/~shuttle/drc/下載可容許錯誤列表
產生測試vector file

## Slide 4: RTL
run ncverilog
function simulation
nWave

## Slide 5: RTL 不可合成 (DC不給過)
reset將所有register array歸零(用for即可)，不然DC合完會unknown。
for( i=0 ; i<=x ; i=i+y ) 這裡x跟y不可為變數。
always@(a) , a必須是此always block內有用到之變數。
同個變數不可放不同的always block內。(multiple driven problem)
不可有latch

## Slide 6: Run ncverilog
1
2
開啟 *.fsdb
選擇欲觀察的波形
RnWave
觀察波型
你的所有設計.v檔
你的測試檔tb.v
DC 及 ICC 再放即可
為了可以產生波形
如果只改部分code
ncverilog只會重新合成改code的地方
加+clear會清掉所有之前合成的
全部重新合成，不然可以會有bug
適合小電路 >Rncverilog your_tb.v your_design00.v your_design01.v +access+r +clear
適合大電路 >Rncverilog –f run.f
為了看波形檔 tb.v必須加入:

## Slide 7: DC
design compile
logic synthesis

## Slide 8: 包IO pad (T18)
cad/CBDK/CBDK_TSMC018_Arm_v4.0/CIC/doc
(CBDK = Cell-Based Design Kit)
PDIDGZ
PDIDGZ
PDIDGZ
PDIDGZ
PDIDGZ
PDIDGZ
…..
PD016CDG
PD016CDG
PD016CDG
PD016CDG
PD016CDG
PD016CDG
Your
Design
…..
C
C
I
I
I
I
I
I
C
C
C
C
PAD
PAD
PAD
PAD
PAD
PAD
PAD
PAD
PAD
PAD
PAD
PAD
TOP cell
數字代表driving能力
通常選>16以上(16,24..)
太小跑不到100 MHz以上
RTL
DC
ICC
包io pad
dv環境設定
read file
constraints
RTL
DC
ICC
包IO pad
read file
set environment
set constraints
compile
analysis
report
Design Setup

## Slide 9: Rdv - Design Setup
只能在有.synopsys_dc.setup檔的資料夾下run Rdv (or dc_shell -gui)
.synopsys_dc.setup (0.18um TSMC/ARM為例)
補充1:
.18TSMC是由ARM提供cell library
.18UMC是由Faraday(智元科技)提供
補充2:
.lib檔 -> Cadence
.db檔->Synopsys
core library: slow.db (Max delay-setup time)
fast.db (Min delay-hold time)
IO pad library: tpz973gvwc.db
tpz973gvbc.db
bounding pad: tpb*
合成mapping用
wc=worst case
bc=best case
查詢lib資料時使用
($:變數內容值)
design ware library的現成IP(例sin, cos…)
Synopsys內建的
產生schematic用
(path: cad/synopsys/synthesis/cur/dw/doc/datasheets)
Name | Temp | Volt
slow | 125 | 1.62
typical | 25 | 1.8
fast | -40 | 1.98
wc v.s. bc
-10%
+10%
RTL
DC
ICC
包io pad
dv環境設定
read file
constraints
RTL
DC
ICC
包IO pad
read file
set environment
set constraints
compile
analysis
report
Design Setup

## Slide 10: Read File - Scripts
此時會報.v檔是否有語法上的錯誤 (DC不可合)
檢查是否有latch
RTL
DC
ICC
包io pad
dv環境設定
read file
constraints
RTL
DC
ICC
包IO pad
read file
set environment
set constraints
compile
analysis
report
Design Setup
source scripts

## Slide 11: Set Environment
set_operating_conditions
1
set_input_delay
2
set_driving_cell
3
set_load
4
set_output_delay
5
set_wire_load_model
6
create_clock
My design
RTL
DC
ICC
包io pad
dv環境設定
read file
constraints
RTL
DC
ICC
包IO pad
read file
set environment
set constraints
compile
analysis
report
Design Setup

## Slide 12: Set input delay and output delay
clk
FF1
FF2
FF3
FF4
3ns
7ns
2ns
8ns
10ns
My design
B design
A design
set_input_delay –clock clk –max 3 [get_ports in]
set_output_delay –clock clk –max 8 [get_ports out]
RTL
DC
ICC
包io pad
dv環境設定
read file
constraints
RTL
DC
ICC
包IO pad
read file
set environment
set constraints
compile
analysis
report
Design Setup

## Slide 13: Set Environment - Scripts
T18的driving cell是PDIDGZ
V93000機台的load 是 40
跟前後design之間的delay
因APR route後才會有真正的net delay
這裡必須先設wire load model for net delay
請設wl10 (誤差最小)
clock uncertainty = clock skew 通常設0.1~0.3
= clock network latency 內部delay 通常設1~3
input transition固定設0.5 (TSRI V93000機台)
clock transition 通常設0.1~0.3
包完IO pad的TOP cell name
20 ns = 50 MHz
檢查timing 是否 slack>=0
input delay同常設1/3~1/2 period
RTL
DC
ICC
包io pad
dv環境設定
read file
constraints
RTL
DC
ICC
包IO pad
read file
set environment
set constraints
compile
analysis
report
Design Setup

## Slide 14: Set Constraints
用多核心跑合成，提升合成速度。
檢查multiple instance problem
uniquify command一下即可修正此problem 但會因此將net 及cell 名稱都打亂
如果為了debug要保留內部pin原名稱
請下
set compile_preserve_subdesign_interfaces true
RTL
DC
ICC
包io pad
dv環境設定
read file
constraints
RTL
DC
ICC
包IO pad
read file
set environment
set constraints
compile
analysis
report
Design Setup

## Slide 15: Compile
RTL
DC
ICC
包io pad
dv環境設定
read file
constraints
RTL
DC
ICC
包IO pad
read file
set environment
set constraints
compile
analysis
report
DC跑完會產生以下的檔:
_syn.v :合成完的gate-level netlist (run function simulation)
.sdf :會有cell的setup/ hold time資訊
.ddc
.sdc :會有你下的constraints
非常不建議用compile_ultra command,常常合成出來的function會fail
Change naming rule
Design Setup

## Slide 16: 計算gate counts
RTL
DC
ICC
包io pad
dv環境設定
read file
constraints
RTL
DC
ICC
包IO pad
read file
set environment
set constraints
compile
analysis
report
cad/CBDK/CBDK_TSMC018_Arm_v4.0 \
/CIC/doc
找NAND21的datasheets資訊
T18的NAND21面積約是9.9792 um2
gate counts =
chip cell area
NAND21 area
cell area 不是 total area
Design Setup

## Slide 17: report_power
RTL
DC
ICC
包io pad
dv環境設定
read file
constraints
RTL
DC
ICC
包IO pad
read file
set environment
set constraints
compile
analysis
report
Dynamic power:
(1)Switch power
(2)Internal power
1. short circuit : pmos and nmos 0<->1會有瞬間兩個都導通
2. charging internal load 充放電
通常core power都10 mW以下
Design Setup

## Slide 18: report_timing
RTL
DC
ICC
包io pad
dv環境設定
read file
constraints
RTL
DC
ICC
包IO pad
Design Setup
read file
set environment
set constraints
compile
analysis
report
檢查setup time >report_timing
修setup time violation >compile –incremental_mapping –map_effort high
檢查hold time >report_timing –delay_type min
修hold time violation >compile –inc –only_hold_time
setup time and hold time 的 slack都必須>=0 ! (最好不要剛好=0)

## Slide 19: DC simulation
Rncverilog –f run_syn.f
RnWave
如果跑不對，可能要修RTL code，從nWave看波形哪裡錯了，很有可能出錯會是latch或是combinational block的地方。

## Slide 20: ICC
IC compile
APR

## Slide 21: Design Setup
DC
Design Setup
ICC
Design Planning
Placement
CTS
Routing
DFM
一樣必須在有.synopsys_dc.setup檔案下的資料夾才能 run Ricc_shell -gui
Create library
Import design (*_syn.v) : 將用DC合成完的netlist檔讀進來
TLU+
Read constraints (.sdc)
FRAM是假layout 精簡版的layout只有metal1 layer以上(保護製程機密)
.tf是製程參數檔 裡面有關於每層metal的相關資訊 等等
tpz*是IO pad; tpb*是 bounding pad
自己命名library name

## Slide 22: Create Starting Floorplan (T18)
DC
Design Setup
ICC
Placement
Create physical-only pad cells
Specify pad cell locations (io.tdf)
IR drop
power network
congestion
Course placement
Floor Plan
Design Planning
設定四個corner
DGZ: Digital
1: core pad
2: IO pad
TSMC有一個IO要用POC
補充
IO power pad 擺放要四邊平均且交錯擺放。
(Shielding)
CTS

## Slide 23: io.tdf
core area
cornerLL
cornerLR
cornerUR
cornerUL
Side 1
Side 3
Side 2
Side 4
1 2 3 4 5
1 2 3 4 5
1 2 3 4 5
1 2 3 4 5
min_right_iospace
min_left_iospace
DC
Design Setup
ICC
Placement
IR drop
power network
congestion
Course placement
Floor Plan
Design Planning
CTS

## Slide 24: Create Starting Floorplan (T18)
Initialize the floorplan
Insert pad filler cells
core utilization =
pad間有空隙會導致開路，必須放 pad filler cells接起來。
core跟pad的空隙=長power ring的地方 ; 注意U18一定要>=80 um
standard cell area + macro cell area
core area
must be from bigger to smaller
DC
Design Setup
ICC
Placement
IR drop
power network
congestion
Course placement
Floor Plan
Design Planning
CTS

## Slide 25: Course Placement
只是初步的擺放(會在chip外)
timing優化
DC
Design Setup
ICC
Placement
IR drop
power network
congestion
Course placement
Floor Plan
Design Planning
CTS

## Slide 26: Analyze Congestion
分析congestion狀態，點選Global Route Congestion視窗，再按下reload。
越紅色表示越嚴重。
通常layer 1-3可忽略，layer 4-5可能需要改善。
DC
Design Setup
ICC
Placement
IR drop
power network
congestion
Course placement
Floor Plan
Design Planning
CTS

## Slide 27: Optimize Congestion
觀察發生位置:如果在standard cell的地方，可以等placement步驟解決。
如果在macro附近，可以增加macro附近的空隙:
>set physical_hard_keepout_distance 10
>set_keepout_margin –type hard –outer {10 0 10 0} RAM5
或是降低core utilization
加大距離
DC
Design Setup
ICC
Placement
IR drop
power network
congestion
Course placement
Floor Plan
Design Planning
CTS

## Slide 28: Synthesis Network Power
長power ring/ power strap
水平:metal3 垂直:metal2
3:水平 2:垂直
分析IR drop
DC
Design Setup
ICC
Placement
IR drop
power network
congestion
Course placement
Floor Plan
Design Planning
CTS

## Slide 29: Analyze IR drop
越紅色越嚴重
單位 :mV
不能超過10% 的VDD(例1.8V*10%=0.18V=180mV)
DC
Design Setup
ICC
Placement
IR drop
power network
congestion
Course placement
Floor Plan
Design Planning
CTS

## Slide 30: Synthesis Network Power
將power ring連接至power pad
長power rail
再分析一次IR drop
gap是指兩個VDD/VSS的距離
設定strap下不要擺放standard cells
DC
Design Setup
ICC
Placement
IR drop
power network
congestion
Course placement
Floor Plan
Design Planning
CTS

## Slide 31: Placement
補充
tie cell是指將常數0或1的pin不接到VDD或VSS，而是接tie cell(較穩定)
先將delay設為0查看constraint狀態，transition(推動力) violation可以先忽略，等CTS解決
在CTS前一律都是用.sdc的constraints
確認之前的步驟都沒錯，檢查error是0, warning沒關係
source完warning很多是正常，可忽略
再檢查一次congestion
slack>=0
重新改scan chain因為真正placement後排列與DC不同
確認將VDD VSS都接到power pad
DC
Design Setup
ICC
Design Planning
CTS
Placement
Routing
DFM
Export

## Slide 32: Placement – congestion problem
如果有congestion problem:
  如果slack<0請下 >refine_placement –perturbation_level high
  > psynopt
  否則下 >refine_placement
  或 >refine_placement –congestion_effort low|medium|high
記住: 先修congestion再修timing
修timing下 >psynopt
或 >place_opt
DC
Design Setup
ICC
Design Planning
CTS
Placement
Routing
DFM
Export

## Slide 33: CTS – Clock Tree Synthesis
Inserts buffers to meet skew(uncertainty), latency and transition(推動力) goals.
CTS前都是吃.sdc來分析,CTS後便是實際加buffers的結果。
亦可以修正hold time violation.
檢查CTS前的步驟是否 0 error
修hold time
transition violation可以忽略(推動力問題)CTS後會改善
將新create的buffers連接power pad
DC
Design Setup
ICC
Design Planning
CTS
Placement
Routing
DFM
Export

## Slide 34: Routing
redundant via: 防止製程飄移，打double vias
T90,T18,U18 都是HVH
  M1,M3 … :Horizontal
  M2,M4 … :Vertical
確認routing前沒error,注意這error/warning在IO pad內可忽略!
auto route雖然較快但不建議，建議使用route_opt
檢查antenna rule (U18製程則無此步驟)
DC
Design Setup
ICC
Design Planning
CTS
Placement
Routing
DFM
Export

## Slide 35: Check DRC rules
如open nets以及DRC violations:
  確認執行過(command) >verify_zrt_route
  (gui) Route >Detail Route >√Incremental routing √Initial DRC from input cell
  (gui) OK
如果還是無法解決，請刪掉所有route重新下route_opt
  (gui) Route >Delete Route > √ Detailed route √Global route
  (command) >route_opt –effort high
DC
Design Setup
ICC
Design Planning
CTS
Placement
Routing
DFM
Export

## Slide 36: DFM – Design For Manufacturing
目的: 增加晶片製作良率。
方式: 加入core filler平均chip density即可增加良率。
加入core filler cells
自動加text
3:打在metal 3的text
加入filler cells後可能會有route DRC violation,故必須再檢查一次
DC
Design Setup
ICC
Design Planning
CTS
Placement
Routing
DFM
Export

## Slide 37: 打text
打text : VDD VSS (T18) / VCC GND (U18)
VDD及VSS各打一個就好
輸入VDD/ VSS
Text vis.要打勾
選Apply
不要選Auto select 自己選擇layer, 大小輸入5.0
在VDD打VDD,VSS打VSS
6
5
4
2
1
3
按shift+t
DC
Design Setup
ICC
Design Planning
CTS
Placement
Routing
DFM
Export

## Slide 38: 打text
打text : IOVDD IOVSS (T18) / IOVCC IOGND (U18)
IOVDD及IOVSS各打一個就好
注意!一定要打在+上面!
Pin vis.要打勾
1
輸入IOVDD 及IOVSS
不要選Auto select 自己選擇layer, 大小輸入5.0
選Apply
2
3
按shift+t
6
5
4
打在io vdd 及io vss上
一定要打在+上
DC
Design Setup
ICC
Design Planning
CTS
Placement
Routing
DFM
Export

## Slide 39: Add Bounding Pad
注意!此步驟run結果會是0，而且有undo的warning都請忽略!
確認完成方式:將level調成1,即可觀察bounding pad是否有加上去。
DC
Design Setup
ICC
Design Planning
CTS
Placement
Routing
DFM
Export

## Slide 40: Export
DC
Design Setup
ICC
Design Planning
CTS
Placement
Routing
DFM
輸出檔案以及建議名稱:
*_pr.gds 將作Tape Out的步驟檔後測DRC。
*_pr.v 拿來跑function simulation(post-sim) 及LVS比對。
*_pr.sdf 會有cell的setup/ hold time資訊。
pr表示APR跑完的結果，與DC跑完的_syn作區別。
Export

## Slide 41: Post Simulation
Rncverilog –f run_route.f
RnWave

## Slide 42: Tape Out & Qserver
DRC
LVS

## Slide 43: Add Bounding Pad(T18)
> Rlaker &
(GUI) File >Import >stream …
/PDK/T18/Laker/Laker_MM*_2.7c.tf
ICC跑完的.gds檔
之前Lib名稱
RTL
DC
ICC
Add Bounding Pad
LVS
Qserver
DRC

## Slide 44: Add Bounding Pad(T18)
File >Import >stream …
注意! 此步驟千萬不要open著layout, 會lock住無法import
依序加入:
tsmc18_core.gds
tpz973gv.gds
tpb973gv_cic.gds
RTL
DC
ICC
Add Bounding Pad
LVS
Qserver
DRC

## Slide 45: Add Bounding Pad(T18)
觀察是否成功:
  (GUI) open > … 選你的layout
  按 shift+f and ctrl+f 切換觀察bounding pad是否加上
shift+f
ctrl+f
import前
import成功後
RTL
DC
ICC
Add Bounding Pad
LVS
Qserver
DRC

## Slide 46: Add Bounding Pad(T18)
(GUI) File >Export >stream …
建議名稱*_merge.gds
這個GDS檔將會拿去做DRC驗證及LVS比對，也是將上傳至TSRI的最終下線晶片檔。
命名新名稱,建議*_merge.gds
RTL
DC
ICC
Add Bounding Pad
LVS
Qserver
DRC

## Slide 47: LVS
>mkdir verify 創建資料夾
>mkdir lvs
>cd ~/lvs
>cp your_path/*_merge.gds . 將最終版的GDS檔copy過來
>cp your_path /*_pr.v . 將ICC合成完的.v檔copy過來
將*_pr.v所有的IOVDD IOVSS註解掉 (很重要一定要做) *記住:先註解掉再轉檔*
將.v檔轉成.spi
  > Rv2lvs -64 –v *_pr.v –l tsmc18_lvs.v –l tpz973gv_lvs.v –l tpb973gv_lvs.v \
  –s tsmc18_lvs.spi –s tpz973gv_lvs.spi –s tpb973gv_lvs.spi \
  –s1 VDD –s0 VSS –o source.spi
修改T18_LVS_CB.rule檔
比對LVS
  > Qcalibre –lvs -64 –spice layput.spi –hier –turbo_all –auto T18_LVS_CB.rule
在LVS_result內查看lvs.rep檔 確認correct (將上傳至TSRI)
修改T18_LVS_CB.rule
請確認資料夾底下有這些檔案，沒有的話
請至學長姊的資料夾copy:
tsmc18_lvs.v
tpz973gv_lvs.v
tpb973gv_lvs.v
tsmc18_lvs.spi
tpz973gv_lvs.spi
tpb973gv_lvs.spi
ICC跑完的.v檔
-o表示要output的檔案名稱
剛剛Rv2lvs的output檔名稱
add bounding pad完的GDS
RTL
DC
ICC
Add Bounding Pad
LVS
Qserver
DRC

## Slide 48: Qentry DRC – 真layout DRC
由於製程layout不公開，CBDK的layout都只有m1 layer以上(Phantom)
，故必須上傳至Qserver換成完整layout跑DRC verification.
> cd ~/verify
> mkdir drc
> cd drc
> cp your_path/*_merge.gds . 將tape out的GDS檔複製過來
> Qentry –M DRC –tech TSMC18 –f *_merge.gds –c TSMC18 –i TSMC18 \
–addTagCell –addDummyCell
> showq
直到你的帳號消失，表示完成。
將DRC_result底下含DRC.db檔先copy進自己的目錄下
addTagCell:
晶片左下角的記號，辨認晶片方向
addDummyCell : (U18不加)
加入dummy cells，均勻chip density
RTL
DC
ICC
Add Bounding Pad
LVS
Qserver
DRC

## Slide 49: DRC
>Rlaker
(GUI) File >Import >stream …
(GUI) Open> … 選你的layout
(GUI) Verify >Calibre >Start RVE
(GUI) 選DRC.db檔
至TSRI下載DRC可容許錯誤列表(假錯list)
確認完error皆為可容錯，截圖。
上傳檔案是DRC.rep
RTL
DC
ICC
Add Bounding Pad
LVS
Qserver
DRC

## Slide 50: TSRI V93000
test pattern
vector file
腳位

## Slide 51: Vector file
注意FORMAT的順序一定要跟下面的順序一樣。
用RTL或DC跑完的.v檔產生皆可。
輸入皆為1及0.
輸出則為H/L/X.
1/0/H/L/X 會在timing file中定義 (timing file不用準備)
範例如下:

## Slide 52: 產生vector tb參考

## Slide 53: Timing file (不用準備)
圖片出處: Digital Chip Testing with Agilent 93000 SOC Series (上)

## Slide 54: Prepare for DUT Board Connection