## Slide 1
學生：蘇柏丞
AES-128

## Slide 2
目錄
contents
01
AES介紹
02
硬體架構
03
合成結果
04
改善方向

## Slide 3
AES介紹
01

## Slide 4
AES 介紹
對稱加密
數學運算相對複雜低，使得硬體成本較低，速度也較快
使用伽羅瓦有限場進行乘法與加法運算
sender
plaintext
recipient
plaintext
Encrypt
Decrypt
ciphertext
ciphertext
key
transmission
13

## Slide 5
伽羅瓦有限場
基於二元，且每次處理資料的單位為8個位元
加法運算「+」：元素之間進行位元互斥或
乘法運算「 ‧ 」：使用分配律將被乘數的項次拆開各自相乘運算後，再將各自結果相加起來
13

## Slide 6
AES Algorithm
14
Two important parts：
Key expansion
Message encryption
AES-128 | 
Key size | 128 bits
Plaintext block size | 128 bits
Number of rounds | 10
Round key size | 128 bits
Number of expanded keys | 44
Key Expansion
AddRoundKey
SubBytes
ShiftRows
MisColumns
AddRoundKey
Round 1
SubBytes
ShiftRows
AddRoundKey
Round r
SubBytes
ShiftRows
MisColumns
AddRoundKey
Round ()
…
Plaintext
Key
Ciphertext
W[0, 3]
W[4, 7]
W[4(Nr-1), 4(Nr-1)+3]
W[4Nr, 4Nr+3]

## Slide 7
AES Algorithm – Substitute Bytes
S-box |  | Column |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | a | b | c | d | e | f
Row | 0 | 63 | 7c | 77 | 7b | f2 | 6b | 6f | c5 | 30 | 01 | 67 | 2b | fe | d7 | ab | 76
 | 1 | ca | 82 | c9 | 7d | fa | 59 | 47 | f0 | ad | d4 | a2 | af | 9c | a4 | 72 | c0
 | 2 | b7 | fd | 93 | 26 | 36 | 3f | f7 | cc | 34 | a5 | e5 | f1 | 71 | d8 | 31 | 15
 | 3 | 04 | c7 | 23 | c3 | 18 | 96 | 05 | 9a | 07 | 12 | 80 | e2 | eb | 27 | b2 | 75
 | 4 | 09 | 83 | 2c | 1a | 1b | 6e | 5a | a0 | 52 | 3b | d6 | b3 | 29 | e3 | 2f | 84
 | 5 | 53 | d1 | 00 | ed | 20 | fc | b1 | 5b | 6a | cb | be | 39 | 4a | 4c | 58 | cf
 | 6 | d0 | ef | aa | fb | 43 | 4d | 33 | 85 | 45 | f9 | 02 | 7f | 50 | 3c | 9f | a8
 | 7 | 51 | a3 | 40 | 8f | 92 | 9d | 38 | f5 | bc | b6 | da | 21 | 10 | ff | f3 | d2
 | 8 | cd | 0c | 13 | ec | 5f | 97 | 44 | 17 | c4 | a7 | 7e | 3d | 64 | 5d | 19 | 73
 | 9 | 60 | 81 | 4f | dc | 22 | 2a | 90 | 88 | 46 | ee | b8 | 14 | de | 5e | 0b | db
 | a | e0 | 32 | 3a | 0a | 49 | 06 | 24 | 5c | c2 | d3 | ac | 62 | 91 | 95 | e4 | 79
 | b | e7 | c8 | 37 | 6d | 8d | d5 | 4e | a9 | 6c | 56 | f4 | ea | 65 | 7a | ae | 08
 | c | ba | 78 | 25 | 2e | 1c | a6 | b4 | c6 | e8 | dd | 74 | 1f | 4b | bd | 8b | 8a
 | d | 70 | 3e | b5 | 66 | 48 | 03 | f6 | 0e | 61 | 35 | 57 | b9 | 86 | c1 | 1d | 9e
 | e | e1 | f8 | 98 | 11 | 69 | d9 | 8e | 94 | 9b | 1e | 87 | e7 | ce | 55 | 28 | df
 | f | 8c | a1 | 89 | 0d | bf | e6 | 42 | 68 | 41 | 99 | 2d | 0f | b0 | 54 | bb | 16
b7 | b6 | b5 | b4 | b3 | b2 | b1 | b0
S(r , c)
S-box
Y
Y
X
X
S-Box
15

## Slide 8
AES Algorithm – Shift Rows
16
ShiftRows ()

## Slide 9
AES Algorithm – Mix Columns
17
MixColumns ()

## Slide 10
AES Algorithm – Add Round Keys
18

## Slide 11
AES Algorithm – Key Expansion
19

## Slide 12
硬體架構
02

## Slide 13
AES Module
20

## Slide 14
合成結果
03

## Slide 15
AES DC Result
20
Specification | Spec. | Pre-sim
Frequency () | 100 | 100
Power () | 20 | 2.5726
Area () | < 1.44 | 0.1849
Specification | Spec. | Pre-sim
 | 20 | 
 | < 1.44 | 0.1849
Power
Area
Timing

## Slide 16
在這裡鍵入方程式。
AES DC Result
20

## Slide 17
改善方向
04

## Slide 18
教育性晶片下線經驗-AES
Look-up Functionality
Direct Logical Mapping
Composite Field Operation
Multiplicative Inverse + Affine Transformation
4
4
4
4
8
data_in
8
8
&
affine
data_out
06

## Slide 19
教育性晶片下線經驗-AES
If , is the multiplicative inverse of .
the multiplicative inverse can be computed using Equation.
The irreducible polynomial is .
Source : E. NC Mui, “Practical Implementation of Rijndael S-Box Using Combinational Logic,” unpublished draft.
Multiplicative inverse
4
4
4
4
8
data_in
8
data_out
8
06

## Slide 20
教育性晶片下線經驗-AES
Affine transformation
06